## Slide 1
1
2
3
4
5
6
7
8
9
Panel 1: Strategic decarbonisation options
Panel 2: Uncertainty-aware system modelling
Panel 3: Hierarchical decomposition for large-scale optimization
Panel 4: Input data management
Panel 5: Candidate energy technologies and infrastructure list
Panel 6: Temporal resolution and clustering techniques
Panel 7: Optimization framework and objective function
Panel 8: Solver integration and computational settings
Panel 9: Output processing and interactive visualisation
By running the GUI, the first step requires the user to select a heat decarbonization pathway from the available options.
To capture the uncertainty of heat demand and renewable energy availability, different optimization approaches are provided, enabling the user to make robust decisions against uncertain parameters.
To reduce model size/ runtime, GUI offers decomposition techniques, allowing user to choose a preferred method
The user must upload or drag in the input file corresponding to the selected method, with the option to modify it beforehand.
We offer a comprehensive range of technologies and infrastructure across all sectors where the user can include/exclude them in the optimisation model
The user is required to input the desired number of representative days for clustering and scenario generation/reduction.
All optimization coding for all methods is excluded from this layer
User can easily select the desired solver without requiring a license
Visualisation
Hybrid
Electrification
Hydrogenation
Decarbonisation Pathway
Robust
Stochastic
Deterministic
Optimisation Approach
Hierarchical 2
Hierarchical 1
Monolithic
Decomposition Methods
Input number of time-slice
Input number of Scenario
Input number of
representative
day
Clustering and Scenario
Solar
Input data: List of Components
Execute the model
Sets, parameters, variables, objective and constraints are defined in Pyomo
Select Solver
Remote Server:
NEOS
Host Machine:
Gurobi
CPLEX
HiGHS
GLPK
Select Solver
The GUI visualises interactive results within the energy dashboard platform
Wind
Onshore
Wind
Offshore
Hydro
Gas Boiler
H2 Boiler
Hybrid Boiler
ASHP
H2-ASHP
Nuclear
CCGT
OCGT
CCGTCCS
H2CCGT
Coal
Fuel Cell
Biomass
SMRCCS
ATRCCS
BECCS
Electrolyser
Importing Hydrogen
Importing Power
CO2 Pipeline
H2 Pipeline
Power Line
Road Transport
Electrical Storage
H2 Storage
CO2 Reservoir